## Slide 1: Agenda
What’s a Microcontroller?
Types of Microcontrollers
Features and Internal structure of PIC 16F877A Instruction Execution
1

## Slide 2: What is a microcontroller?
A microcontroller (sometimes abbreviated µC, uC or MCU) is a small computer on a single integrated circuit containing a processor core, memory, and programmable input/output peripherals.
It can only perform simple/specific tasks.
A microcontroller is often described as a ‘computer-on-a- chip’.
2

## Slide 3: Microcomputer system and Microcontroller based system
3

## Slide 4: Microcontrollers..
Microcontrollers are purchased ‘blank’ and then programmed
with a specific control program.
Once programmed the microcontroller is build into a product to make the product more intelligent and easier to use.
A designer will use a Microcontroller to:
  Gather input from various sensors
  Process this input into a set of actions
  Use the output mechanisms on the microcontroller to do
something useful.
4

## Slide 5: Types of Microcontrollers
Parallax Propeller
Freescale 68HC11 (8-bit)
Intel 8051
Silicon Laboratories Pipelined 8051 Microcontrollers
ARM processors (from many vendors) using ARM7 or Cortex-M3 cores are generally microcontrollers
STMicroelectronics STM8 (8-bit), ST10 (16-bit) and STM32 (32-bit)
Atmel AVR (8-bit), AVR32 (32-bit), and AT91SAM (32-bit)
Freescale ColdFire (32-bit) and S08 (8-bit)
Hitachi H8, Hitachi SuperH (32-bit)
Hyperstone E1/E2 (32-bit, First full integration of RISC and DSP on one processor core [1996])
Infineon Microcontroller: 8, 16, 32 Bit microcontrollers for
automotive and industrial applications.
5

## Slide 6: Types of Microcontrollers..
MIPS (32-bit PIC32)
NEC V850 (32-bit)
Microchip PIC (8-bit PIC16, PIC18, 16-bit dsPIC33/PIC24)
PowerPC ISE
PSoC (Programmable System-on-Chip)
Rabbit 2000 (8-bit)
Texas Instruments Microcontroller MSP 430 (16-bit), C2000 (32-bit),
and Stellaris (32-bit)
Toshiba TLCS-870 (8-bit/16-bit)
Zilog eZ8 (16-bit), eZ80 (8-bit)
etc
6

## Slide 7: Microcontroller Packaging and Appearance
8
From left to right: PIC 12F508, PIC 16F84A, PIC 16C72, Motorola 68HC05B16, PIC 16F877,
Motorola 68000

## Slide 8: PIC Microcontrollers
Peripheral Interface Controller (PIC) was originally designed by
General Instruments
In the late 1970s, GI introduced PIC® 1650 and 1655 – RISC with 30 instructions.
PIC was sold to Microchip
Features: low-cost, self-contained, 8-bit, Harvard structure, pipelined, RISC, single accumulator, with fixed reset and interrupt vectors.

## Slide 9: PIC Microcontroller product family
8-bit microcontrollers
  PIC10
  PIC12
  PIC14
  PIC16
  PIC17
  PIC18
16-bit microcontrollers
  PIC24F
  PIC24H
32-bit microcontrollers
  PIC32
16-bit digital signal
controllers
  dsPIC30
  dsPIC33F

## Slide 10: PIC Microcontroller product family..
The F in a name generally indicates the PICmicro uses flash
memory and can be erased electronically.
The C generally means it can only be erased by exposing the die to ultraviolet light (which is only possible if a windowed package style is used). An exception to this rule is the PIC16C84 which uses EEPROM and is therefore electrically erasable.

## Slide 11: An Example: PIC16F877
Why PIC16F877A is very popular?
This is because PIC16F877A is very cheap. Apart from that it is also very easy to be assembled. Additional components that you need to make this IC work is just a 5V power supply adapter, a 20MHz crystal oscillator and 2 units of 22pF capacitors.
What is the advantages of PIC16F877A?
This IC can be reprogrammed and erased up to 10,000 times.
Therefore it is very good for new product development phase.
What is the disadvantages of PIC16F877A?
This IC has no internal oscillator so you will need an external crystal of other clock source.
12

## Slide 12
Features
13
Key Features | PIC16F877
MAX Operating Frequency | 20MHz
FLASH Program Memory (14-bit words) | 8K
Data Memory (bytes) | 368
EEPROM Data Memory (bytes) | 256
I/O Ports | RA0-5 (6) RB0-7 (8) RC0-7 (8) RD0-7 (8) RE0-2 (3)
Timers | 3
CCP ( Capture/Compare/PWM) | 2
Serial Communications | MSSP, USART
Parallel Communications | PSP
10-bit Analog-to-Digital Module | 8 Channels
Instruction Set | 35 Instructions
Pins (DIP) | 40 Pins

## Slide 13
Bubble diagram of PIC16F877
14

## Slide 14: Pin Diagram of PIC16F877
Quad Flat Package (QFP)
Plastic Leaded Chip Carrier Package (PLCC)

## Slide 15: Pin Diagram of PIC16F877..
Plastic dual in-line package (DIP)

## Slide 16
PIC16F877
Architecture
17
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 17: PIC16F877 Internal Block Diagram
The basic architecture of PIC16F877 consists of Program
memory, file registers and RAM, ALU and CPU registers.
18
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 18: Memory of the PIC16F877
divided into 3 types of memories:
Program Memory – A memory that contains the program (which we had written), after we've burned it. As a reminder, Program Counter executes commands stored in the program memory, one after the other.
Data Memory – This is RAM memory type, which contains a special registers like SFR (Special Function Register) and GPR (General Purpose Register). The variables that we store in the Data Memory during the program are deleted after we turn off the micro. These two memories have separated data buses, which makes the access to each one of them very easy.
Data EEPROM (Electrically Erasable Programmable Read- Only Memory) – A memory that allows storing the variables as a result of burning the written program.
19
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 19: Memory of the PIC16F877..
Each one of them has a different role. Program Memory and Data Memory two memories that are needed to build a program, and Data EEPROM is used to save data after the microcontroller is turn off.
20
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 20: PIC16F877A Program Memory
Is Flash Memory
Used for storing
compiled code (user’s program)
Program Memory
capacity is 8K x 14 bit 
Each location is 14 bits long
 Every instruction is
coded as a 14 bit word
PC can address up to 8K addresses
Addresses H’000’ and
H’004’ are treated in a special way
21
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 21: PIC16F877A Data Memory (RAM)
Memory storage for variables
Data Memory is also known as Register File and consists of two components.
  General purpose register file (same as RAM).
  Special purpose register file (similar to SFR in 8051).
Addresses range from 0 to 511 and partitioned into 4 banks
 each bank extends up to 7Fh (128 bytes).
The user can only access a RAM byte in a set of 4 banks and
only one bank at a time. The default bank is BANK0.
To access a register that is located in another bank, one should access it inside the program. There are special registers which can be accessed from any bank, such as STATUS register.
22
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 22: PIC16F877A Registers
Some CPU Registers:
  W
  PC
  FSR
  IDF
  PCL
  PCLATH
  STATUS
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 23: W Register
W, the working register, is used by many instructions as the
source of an operand. This is similar to accumulator in 8051.
It may also serve as the destination for the result of the instruction execution. It is an 8-bit register.
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 24: Program Counter
Program Counter (PC) is 13 bit and capable of addressing an 8K word
x 14 bit program memory space.
PC keeps track of the program execution by holding the address of the current instruction.
It is automatically incremented to the next instruction during the
current instruction execution.
Program Counter Stack
an independent 8-level stack is used for the program counter.
As the PC is 13-bit, the stack is organized as 8x13bit registers.
When an interrupt occurs, the PC is pushed onto the stack. When the interrupt is being served, other interrupts remain disabled. Hence, other 7 registers of the stack can be used for subroutine calls within an interrupt service routine or within the mainline program.
25
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 25: FSR & INDF
FSR Register
(File Selection Register, address = 04H, 84H)
is an 8-bit register used as data memory address pointer. This
is used in indirect addressing mode.
INDF Register
(INDirect through FSR, address = 00H, 80H)
INDF is not a physical register. Accessing INDF is actually access the location pointed to by FSR in indirect addressing mode.
26
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 26: PCL & PCLATH
PCL Register
(Program Counter Low Byte, address =02H, 82H)
PCL is actually the lower 8-bits of the 13-bit Program Counter. This is a both readable and writable register.
PCLATH Register
(Program Counter LATcH, address = 0AH, 8AH)
PCLATH is a 8-bit register which can be used to decide the upper 5-bits of the PC. PCLATH is not the upper 5bits of the PC. PCLATH can be read from or written to without affecting the PC. The upper 3 bits of PCLATH remain zero and they serve no purpose. When PCL is written to, the lower 5bits of PCLATH are automatically loaded to the upper 5bits of the PC.
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 27: Memory Map Registers
In order to start programming and build automated system, there is no need to study all the registers of the memory map, but only a few most important ones:
  STATUS register – changes/moves from/between the
banks.
  PORT registers – assigns logic values (“0”/”1”) to the ports
  TRIS registers – data direction register (input/output)
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 28: STATUS Register
Is an 8-bit register that stores the status of the processor.
In most cases, this register is used to switch between the banks (Register Bank Select), but also has other capabilities.
IRP - Register Bank Select bit.
RP1:RP0: - Register Bank Select bits.
TO: Time-out bit
PD: Power-down bit
Z: Zero bit
DC: Digit carry/borrow bit
C: Carry/borrow bit
29
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna
Used in conjunction with PIC’s sleep mode

## Slide 29: PIC16F877 Peripheral features
I/O Ports:
  PIC16F877 has 5 I/O ports:
    PORT A has 6 bit wide, Bidirectional
    PORT B, C, D have 8 bit wide, Bidirectional
    PORT E has 3 bit wide, Bidirectional
  In addition, they have the following alternate functions:
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 30: PIC16F877 Peripheral features..
Each port has 2 control registers:
  TRISx sets whether each pin is an input(1) or output(0)
  PORTx sets their output bit levels or contain their input bit levels.
Pin functionality “overloaded” with other features.
Most pins have 25mA source/sink thus it can drive LEDs directly.
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 31: PIC16F877 Peripheral features…
Analog to Digital Converter (ADC)
  Only available in 14bit and 16bit cores
  Fs (sample rate) < 54KHz
  The result is a 10 bit digital number
  Can generate an interrupt when ADC conversion is done
  The A/D module has 4 registers:
    A/D Result High Register (ADRESH)
    A/D Result Low Register (ADRESL)
    A/D Control Register0 (ADCON0)
    A/D Control Register1 (ADCON1)
  Multiplexed 8 channel inputs
    Must wait T acq to change up sampling capacitor.
  Can take a reference voltage different from that of the
controller.
32
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 32: PIC16F877 Peripheral features….
Timer/counter modules
  Generate interrupts on timer overflow
  Can use external pins as clock in/ clock out (ie. for counting
events or using a different Fosc)
  There are 3 Timer/counter modules:
    Timer0: 8-bit timer/counter with 8-bit pre-scaler
    Timer1: 16-bit timer/counter with 8-bit pre-scaler, can be
incremented during SLEEP via external crystal/clock
    Timer2: 8-bit timer/counter with 8-bit period register, pre-scaler and post-scaler.
33
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 33: PIC16F877 Peripheral features…..
Universal Synchronous Asynchronous Receiver
Transmitter (USART/SCI) with 9-bit address detection.
  Asynchronous communication: UART (RS 232 serial)
    Can do 300bps – 115kbps
    8 or 9 bits, parity, start and stop bits, etc.
    Outputs 5V  needs a RS232 level converter (e.g MAX232)
Synchronous communication: i.e with clock signal
  SPI = Serial Peripheral Interface
    3 wire: Data in, Data out, Clock
    Master/Slave (can have multiple masters)
    Very high speed (1.6Mbps)
    Full speed simultaneous send and receive (Full duplex)
  I2C = Inter IC
    2 wire: Data and Clock
    Master/Slave (Single master only)
    Lots of cheap I2C chips available; typically < 100kbps
34
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 34: PIC16F877 Peripheral features…..
Capture, Compare, PWM modules
  Capture is 16-bit, max. resolution is 12.5 ns
  Compare is 16-bit, max. resolution is 200 ns
  PWM max. resolution is 10-bit
Parallel Slave Port (PSP) 8-bits wide, with external RD, WR and CS controls
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 35: Clock and Instruction Cycles
Clock from the oscillator enters a microcontroller via OSC1 pin where internal circuit of a microcontroller divides the clock into four even clocks Q1, Q2, Q3 and Q4 which do not overlap.
These four clocks make up one instruction cycle (also called
machine cycle) during which one instruction is executed.
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 36: Clock and Instruction Cycles..
Execution of instruction starts by calling an instruction that is next in
string.
Instruction is called from program memory on every Q1 and is written in Instruction Register (IR) on Q4.
Decoding and execution of instruction are done between the next Q1 and Q4 cycles. The following diagram shows the relationship between instruction cycle and clock of the oscillator (OSC1) as well as that of internal clocks Q1 – Q4.
Program Counter (PC) holds information about the address of the
next instruction.
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna

## Slide 37: Pipelining in PIC
RTES, Lec#3 , Spring 2015
© Ahmad El-Banna
There are 35 single word instructions. A two-stage pipeline overlaps fetch and execution of instructions. As a result, all instructions execute in a single cycle except for program branches. These take two cycles since the fetch instruction is “flushed” from the pipeline while the new instruction is being fetched and then executed.
A typical picture of the pipeline is shown in Figure 3.
Figure3: Instruction Pipeline Flow

## Slide 38
© Ahmad El-Banna
RTES, Lec#3 , Spring 2015